# Woodwalton Drainage Commissioners Biodiversity Action Plan Report 2013-14

# Drainage Ditch Action Plan

| Target Reference | Target | Action Reference | IDB Actions | Partners | Date | Indicators | Report |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Manage ditches for biodiversity as well as for drainage | 1.1 | Establish and maintain a management plan for routine IDB operations incorporating key biodiversity features | Environmental Officer | 2015 | Plan finalised and followed each year | A map-based plan is in the process of establishment. |
|  |  | 1.2 | Look for opportunities to provide natural erosion protection such as marginal plant ledges when re-profiling ditches | Environmental Officer | Ongoing | If re-profiling is carried out, opportunities identified | No appropriate sites for this method were identified during the period. |
|  |  | 1.3 | Provide natural erosion protection as in 1.2 if opportunities available | Environmental Officer | Ongoing | Length of ditch with ledge / natural vegetation revetment | As above. |
| 2 | Identify ditches of conservation interest and manage appropriately | 2.2 | Ensure appropriate management of ditches for priority species | Environmental Officer, Plantlife, Wildlife Trust | Ongoing | Specified in management plan | Any priority ditches will be identified as the management plan map is developed. |
| 3 | Support the Environmental Officer in working with landowners to benefit wildlife in the district | 3.1 | Refer private landowners to the Environmental Officer for advice on creating field margin buffer zones and wildlife-friendly ditch management | Environmental Officer, Natural England, Wildlife Trust, FWAG | Ongoing | Number of contacts received and passed to Environmental Officer | No formal contacts received. |
| 4 | Control invasive species | 4.1 | Report any sightings of non-native invasive species immediately to the Environmental Officer and control as appropriate (see Appendix F for species list) | Environmental Officer, Environment Agency, Plantlife, Wildlife Trust | Ongoing | Reports to Environmental Officer | No non-native species reported. |

# Reedbed Action Plan

| Target Reference | Target | Action Reference | IDB Actions | Partners | Date | Indicators | Report |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Identify, assess and map any areas of reedbed over 0.5ha in size | 1.1 | Pass details of any known areas to MLC Environmental Officer | Wildlife Trust, Natural England, Environment Agency | 2012 | Review of reedbed areas carried out | No areas of reedbed over 0.5ha identified. |
| 2 | Support appropriate reedbed creation | 2.2 | Manage the District adopted drains, where possible, to assist private landowners who wish to create areas of reedbed on their own land | Wildlife Trust, Environment Agency | Ongoing | (a) Number of requests received (b) Number of landowners assisted | MLC supported the Great Fen Project as a Partner. No other approaches received. |
| 3 | Take conservation value of reedbed into account when planning and carrying out ditch and river maintenance | 3.2 | Where reeds are present, commence mowing or cleansing work outside the bird breeding season (7th April – 15th July). Where reeds are growing in water be aware of the potential for late-nesting reed warblers being present until late August and avoid mowing in that location. In exceptional circumstances where this is not possible, seek advice from the Environmental Officer. | Environmental Officer, Wildlife Trust, RSPB | Ongoing | Reeds not cut during bird nesting season | Reeds or other marginal vegetation were not cut during the bird nesting season. |

# Open Water Action Plan

| Target Reference | Target | Action Reference | IDB Actions | Partners | Date | Indicators | Report |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Promote the creation of ponds, lakes and reservoirs in appropriate areas | 1.1 | Consider pond creation as mitigation when a ditch has to be filled in or culverted | Local authorities, Amphibian & Reptile Conservation, Wildlife Trust | Ongoing | (a) Number of mitigation opportunities (b) Number of ponds created | (a) No ditch infilling occurred, (b) No pond creation opportunities in mitigation necessary. |
|  |  | 1.2 | Support creation of flood storage areas and reservoirs | Environment Agency, Natural England, Wildlife Trust, RSPB | Ongoing | Number of projects involved with | One. As a Partner in the Great Fen Project the Middle Level Commissioners Engineers are involved with the planning for flood event storage in the Great Fen area. |
|  |  | 1.3 | Assist private landowners with advice, information or contacts as necessary | Amphibian & Reptile Conservation, Wildlife Trust | Ongoing | (a) Number of information requests (b) Number responded to | (a) None (b) Nil |
| 2 | Look for opportunities to create open water habitat when managing ditches | 2.1 | Create a pool at an appropriate ditch junction when re-profiling (see the Drainage Channel Biodiversity Manual, technique CL3)) | Environmental Officer | 2010 | One pool successfully created | No opportunities for this on Board drains were identified during the period. The creation of various water areas is being undertaken by the Great Fen Project. |

# Water Vole Action Plan

| Target Reference | Target | Action Reference | IDB Actions | Partners | Date | Indicators | Report |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Manage ditches according to the law and to best practice for water vole | 1.1 | Assume water voles are present when carrying out works (discuss special circumstances with the Environmental Officer) and follow the ADA water vole mitigation guide | Environmental Officer | Ongoing | Measures incorporated in management plans | Water vole friendly ditch maintenance practices were adhered to. |
|  |  | 1.2 | Publicise good practice for rat control near drainage ditches | Environmental Officer, Wildlife Trust | Ongoing | Good practice publicised | Good practice for rat control was publicised via Environmental Officers newsletter issue 5. |
| 2 | Enhance drainage ditch habitat to benefit water vole | 2.1 | Look for opportunities to add a marginal shelf when re-profiling banks | Environmental Officer | Ongoing | (a) Opportunities identified (b) Measures taken | (a) No opportunities identified during the period (b) No measures taken. |
|  |  | 2.2 | Consider using coir roll to stabilise banks and provide marginal vegetation | Environmental Officer | Ongoing | (a) Sites considered (b) Measures taken | No appropriate sites for this measure identified. |
| 3 | Monitor water vole populations | 3.1 | Set up a survey programme to monitor water vole populations | Environmental Officer, Wildlife Trust | 2010 | Surveys carried out | Informal checks are carried out by the EO. Other surveys are being carried out in the Great Fen Project area. |
|  |  | 3.2 | Provide data on water vole to the relevant Biological Records Centres | Environmental Officer, CPBRC, NBIS | Ongoing | Data sent via Environmental Officer annually | Records will be passed on when compiled. |
| 4 | Control mink as necessary | 4.2 | Carry out mink control as part of the Middle Level programme and report all sightings to the Environmental Officer | Environmental Officer | Ongoing | (a) Number of trapping days (b) Number of mink caught | Mink trapping is carried out within the District by landowners. Further trapping by land owners and managers is encouraged within the District. Traps & support available from the Environmental Officer. |

# Otter Action Plan

| Target Reference | Target | Action Reference | IDB Actions | Partners | Date | Indicators | Report |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Improve otter habitat | 1.1 | Identify and maintain existing key bushes and trees near watercourses likely to be important for otters | Environmental Officer | 2012 and ongoing | Sites identified and listed in management plans | Any key bushes and trees will be identified as the management plan map is developed. |
| 2 | Monitor otter populations | 2.3 | Ensure any dead otters are reported to the Environmental Officer and transferred to the Environment Agency for post mortem | Environment Agency | Ongoing | Otters reported to Environmental Officer, if found | No dead otters recorded. Otter signs and sightings on the Great Raveley Drain, on other surrounding drains and in Woodwalton Fen Reserve were more frequent. Otter sightings were more frequent during the period including a female with young. |
| 3 | Reduce otter deaths related to eel and crayfish trapping and road traffic | 3.1 | Report incidents of suspected illegal netting, trapping or fishing to the Environment Agency Fisheries Officers and the MLC Environmental Officer | Environment Agency, Angling Clubs & syndicates | Ongoing | Incidents reported, if discovered | No incidents reported. |

# Bats Action Plan

| Target Reference | Target | Action Reference | IDB Actions | Partners | Date | Indicators | Report |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Improve habitat for bats | 1.1 | Put up at least one bat box at an appropriate site, e.g. a pumping station | Bat Conservation Trust | 2015 | Number of bat boxes sited | One. Target achieved 2012. |
|  |  | 1.2 | Pollard suitable trees to provide bat roosts |  | Ongoing | Number of trees pollarded | Suitable trees to be identified. |
|  |  | 1.3 | Identify potential sites for a bat hibernaculum, e.g. in disused buildings or tunnels | Environmental Officer , Bat Conservation Trust | As opportunities arise | (a) Potential sites looked for (b) Site created | Potential sites are being looked for. |
| 2 | Collect information on bat populations | 2.1 | Monitor bat boxes | Bat Conservation Trust | 2015 onwards | (a) Number of boxes monitored (b) Number of boxes used by bats | (a) One (b) Nil The bat box on the old Conington Mill Pumping Station was checked for occupation. No signs of use. |
|  |  | 2.2 | Pass bat box information to CPBRC and NBIS | Environmental Officer, CPBRC, NBIS | 2015 onwards | Data via Environmental Officer annually | Annual, when data available. |

# Kingfisher Action Plan

| Target Reference | Target | Action Reference | IDB Actions | Partners | Date | Indicators | Report |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Improve the quality of kingfisher habitat | 1.1 | Provide at least one potential nest hole in sheet pilings | Environmental Officer | Ongoing | Number of nest sites provided | A kingfisher hole was drilled in steel piles at Conington Mill PS on 13/05/14. |
|  |  | 1.2 | Leave kingfisher fishing perches where possible (e.g. occasional branch) | Environmental Officer | Ongoing | Number of perch sites left | Many natural perching sites exist on Board drains. |
| 2 | Collect records of kingfisher breeding between March and July | 2.1 | Note sightings of potential breeding kingfisher and pass information to CPBRC and NBIS via the Environmental Officer | Environmental Officer, CPBRC, NBIS | Ongoing | Data sent via Environmental Officer annually | No specific breeding sites identified but kingfishers are regularly active on the drains around the District. |

# Barn Owl Action Plan

| Target Reference | Target | Action Reference | IDB Actions | Partners | Date | Indicators | Report |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Improve the quality of barn owl habitat | 1.1 | Put up at least one barn owl nest box in a suitable location | Wildlife Conservation Partnership | 2015 | Number of nest boxes provided | One. Target achieved 2012. |
|  |  | 1.2 | Pollard suitable trees to provide natural nest sites | Environmental Officer | Ongoing | Number of trees pollarded | Suitable trees to be identified. |
| 2 | Collect records of barn owl presence | 2.1 | Monitor nest boxes for use. Have occupied boxes checked for success by licensed barn owl ringers. | Wildlife Conservation Partnership | 2015 | (a) Number of nest boxes checked by licensed ringers (b) Number of nest boxes used | (a) One, the box on the north west side of Conington Mill old pumping station. (b) The box was used by stock doves in 2013. They produced 3 broods. It had a pair of barn owls occupying it in early 2014. |
|  |  | 2.2 | Pass barn owl box information to CPBRC and NBIS | Environmental Officer, Wildlife Conservation Partnership, CPBRC, NBIS | 2015 | Data sent via Environmental Officer annually | Annual, when barn owl data available. |

# Procedural Action Plan

| Target Reference | Target | Action Reference | IDB Actions | Partners | Date | Indicators | Report |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Provide training on IDB BAP and conservation management of drainage channels for all relevant staff by 2013 | 1.1 | Establish programme of 1-day courses for IDB staff and members | Environmental Officer, Wildlife Trust, Natural England, other specialists | Ongoing | (a) Number of courses held (b) Number of Board members / staff attending courses | (a) One meeting held, the IDB BAP meeting in December 2013. (b)Two. Jonathan Papworth & Russell Wright attended. The next meeting is on Wednesday 03/12/14 at the Oliver Cromwell Hotel, March and is open to all board members. Several speakers will give presentations on topics of local interest. All members are very welcome to attend. |
|  |  | 1.2 | Establish suitable training for contractors’ staff | Environmental Officer, Contractors | As required | Contractors attended training course | No courses since the ditching machine operators’ workshop in June 2010. |
| 2 | Take biodiversity into account when planning and undertaking capital works | 2.1 | Consult with the Environmental Officer and choose the best possible mitigation solutions for biodiversity, e.g. fish-friendly pumps | Environmental Officer | Ongoing | (a) Number of capital schemes undertaken (b) Number of schemes commented on | (a) No capital schemes undertaken by the Board (b) No schemes to comment on. |

Black Poplars

Woodwalton DDCs BAP Plan does not include a target for planting black poplars but some have been planted on the margin of the District at the south end of Monks Lode. If any Board Members are interested in providing a site for this scarce native hardwood it would be of value. Black poplars grow to be a distinctive tree that provides many holes and crevices for wildlife. They were traditionally planted to mark parish and other boundaries.

Sources for supply from local trees of pure (non-hybrid) black poplar stock have been identified by DNA testing. The tests also revealed that some of the trees are of a rare clone type that is important to propagate to maintain the genetic base of the species. Cuttings are taken from the existing trees and planted directly at the new sites. Please contact me if you are able to offer a potential location on your land for this rare tree.

Badgers

Badger activity on the side of the Board’s drain 15-16 north of Conington Mill Pumping Station continued with nine active burrows identified. The Environmental Officer obtained a licence from Natural England to fit one-way doors to exclude the badgers during the July to October licence period. 10 doors were fitted on  20/09/12.  After the period of 21 days of checking for non-activity required by the licence, the tunnels were collapsed with the assistance of Jonathan Papworth on 15th October 2013.

A recent check showed signs of badger activity in reduced numbers at the same location. A licence to carry out exclusions again in 2014 will be applied for.

Cliff Carson   Environmental Officer   13/05/14

# Text boxes

The District drains provide good opportunities for nesting waterfowl such as the pair of mute swans with a nest at the old Conington Mill Pumping Station drain (left) and pairs of mallard and tufted ducks nest prospecting near Speechley’s Pumping Station (right).

A black poplar cutting planted at Speed the Plough, courtesy of Mr Ken Warrington.

A hole was drilled in the piles at the old Conington Mill Pumping Station on 13/05/14 to provide a potential nest site for kingfishers.

A badger tunnel in the process of being collapsed.